## Slide 1: Capturing data from Pulse Heart Rate Sensor using Hyperterminal

## Slide 2
Connect the Sensor to Arduino and hold it as shown. “+” wire of sensor connected to 3.3 V, “-” wire connected to “GND” and the third wire is used for sending data, and here it’s connected to pin A0 :

## Slide 3
Upload the Arduino Code as given below:

## Slide 4
Open the Serial Monitor to check if data is being transmitted:

## Slide 5
Open Hyperterminal Application, from the Hyperterminal zip file. You’ll get the below dialog box. Enter some name and press OK:

## Slide 6
Select the option as shown below from the next dialog box (Select your Arduino port, that is):

## Slide 7
Set Baud Rate as 9600, as is needed for Arduino:

## Slide 8
The screen below is expected to appear. Click on Transfer and select Capture Text:

## Slide 9
Select location where you want to save, and save it as a “.csv” file:

## Slide 10
You can open the file and view the data in excel. A scatter plot has also been show. The data is in a certain range mostly. The left column represents the data from sensor, the right column represents the time in milliseconds.: